EMC Fencing assembly installation

Step 1. Set up the gate post position.

The post of the gate should define it first because the gate need install first. The two posts of Gate should keep 2.11-2.12m distance inside of post.

Step 2. The hole digging

(each hole should be 40 cm to 50 cm depth, then put the cement into the hole)

Step 3. Post fixed

Put the post into the hole, keep the post from the ground around 15cm to 20cm depth.

This will give your distance between the panel and ground 0-5cm.

After the cement gets dry, you should install the gates first.

Step 4.  After install the gates, you may start to install the fence. Each two posts distance should be precisely 2.11m to 2.12m width.